## Slide 1: Script usage
usage: create_netlists.py [-h] [--files FILES] [--max_elements MAX_ELEMENTS] [--name NAME] [--CM CM] [--max_CM MAX_CM] [--debug DEBUGLEVEL]
Creating of random netlist
optional arguments:
-h, --help show this help message and exit
--files FILES Number of circuits to be created. (default: 1)
--max_elements MAX_ELEMENTS Maximum number of elements per circuit. (default: 1000)
--name NAME Base name for circuits to be generated. (default: "rcircuit")
--CM CM If CM=1, generate only Current Mirrors (default: 0)
--max_CM MAX_CM If CM=1, Max number of Current Mirrors to be integrated (default: 1)
--debug DEBUGLEVEL Level for debug messages. (default: 0)

## Slide 2: Script usage - Example
Create 100 netlists with max. 1000 elements and max. 2 current mirrors
  create_netlists.py --max_elements 1000 --files 100 --max_CM 2
  In folder circuits:
    All netlists: *.sp
    Logfiles: *.log -> which CMs were chosen
Create 50 netlists with current mirrors
  create_netlists.py --files 50 --CM 1
  In folder CM_circuits :
    All netlists: *.sp
    Logfiles: *.log -> which CM was chosen

## Slide 3: SPICE Syntax
Resistor: (example)
R67 (net24 net6) R=7.3E4
Element type: R (resistor)
Element name: R67
Connections (pin1, pin2): to nets net24, net6
Parameter: resistance = 7.3E4
Capacitor: (example)
C65 (net24 net23) C=6.7E-8
Element type: C (capacitor)
Element name: C65
Connections (pin1, pin2): to nets net24, net23
Parameter: capacitance = 6.7E-8

## Slide 4: SPICE Syntax
MOSFET: (example)
T64 (net24 net13 net13 0) nfet L=7.93E-6 W=0.52E-6
Element type: T (transistor)
Element name: T64
Connections (drain, gate, source, bulk): to nets net24 net13 net13 0
Type: nfet
Parameters: length = 7.93E-6, width = 0.52E-6

## Slide 5: SPICE Syntax
Resistor: (exemplo)
R1 (net1 net2) R=7.3E4
Tipo do Elemento: R (resistor)
Nome do Elemento: R1
Connections (pin1, pin2): to nets net24, net6
Parameter: resistance = 7.3E4
Capacitor: (example)
C65 (net24 net23) C=6.7E-8
Element type: C (capacitor)
Element name: C65
Connections (pin1, pin2): to nets net24, net23
Parameter: capacitance = 6.7E-8

## Slide 6: SPICE Syntax
MOSFET: (example)
T64 (net24 net13 net13 0) nfet L=7.93E-6 W=0.52E-6
Element type: T (transistor)
Element name: T64
Connections (drain, gate, source, bulk): to nets net24 net13 net13 0
Type: nfet
Parameters: length = 7.93E-6, width = 0.52E-6